## Slide 1
What is LSTM?
Simple Explanation with Real Data
How an AI watches 30 mobile cells every 10 seconds and keeps the Malleswaram 4G/5G network healthy
30
Cells monitored
9
KPIs watched
60s
History per decision
5 possible diagnoses: NORMAL OVERLOAD UNDERLOAD SINR LOW POWER WASTE
agents/kpi_agent/model.py | train.py | kpi_agent.py
1

## Slide 2
Think of LSTM Like a Network Doctor
A doctor does not diagnose from one reading — they look at the trend over time. LSTM does the same.
2
DOCTOR checks a patient
Checks vitals every few minutes
Reviews last 6 readings on chart
Looks at 9 vital signs
Diagnoses: healthy / sick / urgent
Prescribes treatment
LSTM checks a cell
Polls each cell every 10 seconds
Reads last 6 KPI snapshots (60 s)
Watches 9 network KPIs per cell
Classifies: NORMAL / OVERLOAD / SINR_LOW...
Triggers SON action (move cell, alert, DTX)
=
Key Insight: A single reading of PRB = 86% could be a harmless spike — or the start of a real overload. The LSTM sees 6 readings in a row and knows the difference. Rules cannot.

## Slide 3
9 Things the LSTM Watches — Per Cell, Every 10 Seconds
These are the 9 KPI features fed into the model (model.py N_FEATURES = 9)
3
KPI Name
Plain English
Range
Warning Sign
PRB DL %
How busy is the cell?
0% = idle 100% = completely full
>85% for 60s = OVERLOAD
SINR dB
How clear is the signal?
Higher = cleaner signal
<5 dB for 60s = SINR_LOW
Connected UEs
How many phones are connected?
5G cell: up to 900 phones
Very few + high power = POWER_WASTE
Power W
How much electricity is the tower using?
5G idle: ~250 W Full load: ~1000 W
High power + few users = waste
Packet Loss %
How many data packets are being dropped?
Target: <0.1% Overload: >0.5%
Rising with PRB = congestion
Throughput Mbps
How fast is data actually flowing?
5G peak: 3800 Mbps 4G: 150 Mbps
Low despite high PRB = interference
CQI
Channel Quality Indicator (link health score)
0 = terrible 15 = perfect
<5 = poor channel quality
BLER %
Block Error Rate — how many data blocks need resending?
Target: <10% Overload: >8%
High BLER + low SINR = interference
Latency ms
How long does one round-trip take?
Normal: <20 ms Overload: >40 ms
Rising latency = congestion
All 9 values are normalised to 0-1 before feeding into the LSTM (so PRB=94% becomes 0.94 and Power=950W becomes 0.79 — same scale)

## Slide 4
How the LSTM Remembers — Two Types of Memory
Unlike a simple rule, the LSTM carries a memory that updates at every timestep
4
LONG-TERM MEMORY (Cell State)
Carries important signals across all 6 timesteps Example: "PRB has been rising for the last 5 readings" This signal travels from t-50s all the way to t=now without being lost or forgotten
SHORT-TERM MEMORY (Hidden State)
What just happened — passed to the next step Example: "At t-10s the PRB jumped sharply to 89%" This recent event influences the decision at the very next timestep (t=now)
Three gates control both memories at every step:
FORGET GATE
Throw away old info that no longer matters
"Last night's low-traffic readings — forget them"
INPUT GATE
Store something new that just happened
"PRB just jumped to 89% — remember that"
OUTPUT GATE
Decide what to pass forward to next step
"Tell next step: rising PRB trend"

## Slide 5
Bidirectional — The LSTM Reads the 60-Second Window Both Ways
Two LSTMs run in parallel: one reads t-50s to t=now, the other reads t=now back to t-50s
5
t-50s
60%
t-40s
68%
t-30s
75%
t-20s
82%
t-10s
89%
t=now
94%
Forward LSTM reads left to right: "PRB is climbing... 60...68...75...82...89...94" → OVERLOAD coming
Backward LSTM reads right to left: "t=now is 94%, previous steps confirm it was a real sustained trend"
Both readings combined → "6 consecutive rising readings, confirmed from both ends = OVERLOAD"
Without bidirectional:
A one-directional LSTM might see the spike at t=now but not know whether what came before it was a real trend or random noise
With bidirectional:
The backward pass confirms: PRB was rising for ALL 6 steps. This is definitely a real overload — act now with high confidence.

## Slide 6
5 Decisions the LSTM Makes — and What Happens Next
After reading 6 timesteps, the model outputs a probability for each class. The highest wins.
6
0 NORMAL
PRB 40-70% | SINR good | Stable UEs
70% of time
Nothing — network is healthy
1 OVERLOAD
PRB >85% | Packet loss rising | Many UEs
15% of time
Auto-move cell to lightest DU (cooldown: 30s between moves)
2 UNDERLOAD
PRB <20% | Very few users | Wasted capacity
8% of time
Flag as sleep candidate Recommend DTX energy saving
3 SINR LOW
SINR <5 dB | High errors | Poor CQI
5% of time
CRITICAL alert raised Request PCI re-optimisation
4 POWER WASTE
High power | Very few users (<15) | Low PRB
2% of time
WARNING alert Recommend DTX / sleep mode Estimated 35% power saving
Class
KPI Signature
Frequency
SON Action Triggered
MIN_CONFIDENCE = 70% — if the model is less than 70% sure, it logs the finding but does NOT act

## Slide 7
Proof — Validation Test Results (30 runs per scenario, seed=42)
We tested the trained LSTM against 7 synthetic scenarios. Here is what it predicted.
7
4 / 7
Scenarios PASSED (100% confidence)
3 / 7
Scenarios FAILED (expose real gaps)
100%
Confidence on every prediction (LSTM never unsure)
PASS
NORMAL — 5G cell at 50% load
NORMAL
NORMAL
100%
Correct — quiet cell correctly left alone
FAIL
NORMAL — 4G cell at 55% load
NORMAL
UNDERLOAD
100%
4G has fewer UEs/lower power — LSTM thinks it is underloaded (training data was 5G-heavy)
PASS
OVERLOAD — 5G cell at 94% load
OVERLOAD
OVERLOAD
100%
Correct — auto-move would be triggered
FAIL
OVERLOAD — 4G cell at 94% load
OVERLOAD
SINR_LOW
100%
4G throughput (141 Mbps) looks like interference to model (training assumed 5G-scale 3100 Mbps at overload)
PASS
SINR_LOW — interference injected
SINR_LOW
SINR_LOW
100%
Correct — CRITICAL alert + PCI reopt triggered
PASS
POWER_WASTE — ideal (training values)
POWER_WASTE
POWER_WASTE
100%
Correct when given training-distribution values
FAIL
POWER_WASTE — simulator-realistic (1% load)
POWER_WASTE
UNDERLOAD
100%
BUG: simulator power at low load=240W (<500W threshold) Linear power model cannot generate high-power + low-UE combo
Scenario
Expected
LSTM Predicted
Conf
Finding

## Slide 8
Real Deployment — 30-Cell Malleswaram Health Snapshot
Post-KPI-agent rebalancing | DU-MLS-1 @ 88% load | DU-MLS-2 @ 72% | DU-MLS-3 @ 62%
8
DU-MLS-1
12 cells | 88% load
Heavy — was overloaded. KPI agent moved 4 cells away.
DU-MLS-2
10 cells | 72% load
Medium — received some rebalanced cells.
DU-MLS-3
8 cells | 62% load
Light — received some rebalanced cells.
Sample cell health at their DU load (one simulated tick per cell):
Cell ID
DU
Type
PRB%
SINR dB
UEs
Power
Pkt Loss
LSTM Class
MLS_RWS_01
DU-MLS-1
5G n78
88%
8.2
792
887W
0.38%
OVERLOAD
MLS_18C_01
DU-MLS-1
5G n78
83%
10.1
747
851W
0.22%
NORMAL
MLS_SPG_01
DU-MLS-2
5G n78
68%
13.5
612
719W
0.00%
NORMAL
MLS_3MN_02
DU-MLS-2
4G B40
67%
15.2
200
133W
0.00%
NORMAL
MLS_6CR_01
DU-MLS-3
5G n78
57%
15.8
513
649W
0.00%
NORMAL
MLS_MGR_02
DU-MLS-3
4G B40
60%
13.7
180
128W
0.00%
NORMAL
At 88% load, some DU-MLS-1 cells breach 85% PRB threshold and trigger auto-move. DU-MLS-2 and DU-MLS-3 cells stay in NORMAL range after rebalancing.

## Slide 9
How the LSTM Was Trained — Synthetic Data, Realistic Distribution
No live network data needed at training time. Synthetic sequences generated from 5G and 4G KPI profiles.
9
Training Samples per Class
NORMAL
3,500 samples (70%)
OVERLOAD
750 samples (15%)
UNDERLOAD
400 samples (8%)
SINR LOW
250 samples (5%)
POWER WASTE
100 samples (2%)
Rare classes (POWER_WASTE = 2%) use Weighted Sampler so the model learns them too
Training Configuration
Epochs
60
Batch size
256
Optimiser
Adam
LR schedule
Cosine annealing
5G profile
n78, 64T64R, 950W
4G profile
B3/B40, 4T4R, 200W
Sequence drift
Slow drift between steps
Train / Val
80% / 20% split
Saved to
kpi_model.pt
Train time
~2 min on CPU
Each training sequence = 6 timesteps with realistic temporal drift
OVERLOAD example: PRB [91%, 93%, 94%, 93%, 95%, 94%] SINR [11.2, 10.8, 11.1, 10.5, 9.8, 10.2] UEs [705, 718, 712, 722, 715, 720] Small drift between steps teaches the LSTM to detect trends, not just memorise snapshots.

## Slide 10
3 Known Gaps + Summary
The LSTM works well for 5G cells. These gaps were found during validation testing.
10
GAP 1 — POWER_WASTE unreachable in simulator
The simulator uses a linear power model: power scales with load. At low load (1% = 9 UEs), power = 240W. The rule requires power > 500W to fire POWER_WASTE. The LSTM was trained on 880W + 8 UEs — it never sees this in real operation.
Recommended fix: Fix: change simulator to hold near-peak RF power when UEs < threshold (real mMIMO hardware does this)
GAP 2 — 4G cells misclassified
Training data was mixed 5G/4G but OVERLOAD class assumed 5G-scale values (UEs=720, power=940W, throughput=3100 Mbps). A 4G cell at overload has UEs=230, power=195W, throughput=140 Mbps. LSTM sees this as SINR_LOW or UNDERLOAD — not OVERLOAD.
Recommended fix: Fix: separate training and inference paths for 4G vs 5G cells
GAP 3 — SINR_LOW needs real interference injection
The simulator degrades SINR only through load. Co-channel interference (the main real-world cause of SINR_LOW) is not modelled. SINR_LOW at moderate load (the training distribution) cannot be generated naturally.
Recommended fix: Fix: add interference_db env variable per cell in the simulator
LSTM correctly classifies 5G NORMAL, OVERLOAD, and SINR_LOW (interference) at 100% confidence. 4G cells and POWER_WASTE need training data improvements.