## Slide 1
KPI Agent
All KPIs Used — With Simple Definitions
Malleswaram Network · 30 cells · 3 DUs · 1 CU · 18,400 peak UEs
9
LSTM Input KPIs (fed to AI model)
5
Extra KPIs stored (InfluxDB only)
7
DU-level KPIs (infrastructure health)
5
Health States (LSTM output classes)
Source files: agents/kpi_agent/model.py | kpi_agent.py | dev-env/simulators/du/du_simulator.py
NORMAL
OVERLOAD
UNDERLOAD
SINR LOW
POWER WASTE
1

## Slide 2
9 KPIs Fed Into the LSTM Model — At a Glance
model.py FEATURE_NORM | kpi_agent.py extract_features() | All normalised to 0-1 before inference
2
#
KPI Field
Simple English Name
Range
Normal (5G)
Danger Threshold
Linked Alert
1
prb_dl_pct
How busy is the cell?
0 – 100 %
40 – 70 %
> 85 % → OVERLOAD
OVERLOAD / LOAD_BALANCE
2
sinr_db
How clean is the signal?
-5 to +30 dB
15 – 22 dB
< 5 dB → SINR_LOW
SINR_DEGRADATION / PCI_REOPT
3
connected_ues
How many phones connected?
0 – 900
300 – 700
< 15 + high power
POWER_WASTE / DTX_RECOMMEND
4
power_w
How much electricity used?
0 – 1200 W
400 – 700 W
> 500 W + few UEs
POWER_WASTE / DTX_RECOMMEND
5
packet_loss_pct
How many data packets dropped?
0 – 5 %
< 0.1 %
> 0.5 % at overload
OVERLOAD (secondary)
6
dl_throughput_mbps
How fast is downlink data?
0 – 4000 Mbps
1000–2500 Mbps
Low despite high PRB
SINR_LOW (secondary)
7
cqi
Channel quality score (link grade)
0 – 15
10 – 14
< 5 = poor channel
SINR_LOW (secondary)
8
bler_pct
What % of data blocks need resending?
0 – 30 %
< 2 %
> 8 % at overload
OVERLOAD / SINR_LOW
9
latency_ms
How long does one data round-trip take?
0 – 500 ms
< 20 ms
> 40 ms congested
OVERLOAD (secondary)
All 9 values are collected from InfluxDB 'cell_kpi' measurement every poll cycle (POLL_INTERVAL_SEC=10s default). 6 consecutive readings form one LSTM input tensor (shape 1 x 6 x 9).

## Slide 3
KPI 1 — PRB DL % and KPI 2 — SINR dB (Most Decision-Critical)
These two KPIs drive OVERLOAD and SINR_LOW detection. Together they reveal if a cell is busy vs degraded.
3
KPI 1 — PRB DL % (prb_dl_pct)
Physical Resource Block Downlink Percentage
Simple definition: How much of the cell's radio capacity is being used right now? Think of it like seats on a bus: 50% PRB = half the seats taken. 95% = almost full.
PRB Range
0 – 20 %
Very quiet
Off-peak hours, late night
20 – 70 %
Normal operation
Daytime, moderate load
70 – 85 %
Getting busy
Evening peak, monitor
85 – 98 %
OVERLOAD
Action: move cell to lighter DU
Rule threshold: > 85% for one reading (fallback) | LSTM: > 85% sustained for 60s
KPI 2 — SINR dB (sinr_db)
Signal-to-Interference-plus-Noise Ratio
Simple definition: How clear is the radio signal versus background noise? Think of it like trying to hear someone in a noisy room: high SINR = quiet room, low = very noisy.
SINR Range
< 0 dB
Terrible signal
Almost unusable — severe interference
0 – 5 dB
SINR LOW
Action: CRITICAL alert + PCI reopt
5 – 15 dB
Acceptable
Degraded but functional
> 15 dB
Good signal
Normal operation — clear channel
Rule threshold: < 5 dB | LSTM: sustained low SINR at moderate PRB = co-channel interference
Key interaction: High PRB + Low SINR → Overloaded AND interference (worst case) High PRB + Good SINR → Pure OVERLOAD (easy to fix — move cell) Low PRB + Low SINR → Pure interference (not fixed by moving cell)

## Slide 4
KPI 3 — Connected UEs and KPI 4 — Power W
Together these two detect POWER_WASTE: a tower drawing full electricity with almost no users connected.
4
KPI 3 — Connected UEs (connected_ues)
How many phones / devices are actively connected to this cell right now?
Simple definition: The number of active users the tower is serving at this moment. 5G NR cell: up to 900 UEs. 4G LTE cell: up to 300 UEs.
< 15 UEs
Near empty
POWER_WASTE candidate if power still high
15 – 200
Low utilisation
UNDERLOAD — sleep candidate
200 – 700
Normal load
Healthy operation
> 700 UEs
Heavy load
Monitor PRB — approaching OVERLOAD
Real values (Malleswaram 5G cell): 2am off-peak: ~45 UEs | 2pm normal: ~540 UEs | 7pm peak: ~870 UEs
KPI 4 — Power W (power_w)
How much electrical power is the tower's radio unit consuming right now?
Simple definition: The electricity bill of the tower. 5G mMIMO is always-on and power-hungry. 5G 64T64R: 225–1000W. 4G 4T4R: 50–200W.
< 300 W
Low power
4G cell or 5G in low-load state
300–700 W
Normal 5G
5G cell at 30–70% load
700–950 W
High 5G
5G cell near full load
> 950 W
Near peak
Full load — check if OVERLOAD
Real values (Malleswaram 5G n78, idle_power=237W, tx_power=950W): 2am idle: ~250W | 2pm normal: ~650W | 7pm peak: ~940W
POWER_WASTE is detected when BOTH conditions are true at the same time: Power W > 500 W AND Connected UEs < 15 Meaning: the tower is drawing near-full electricity but serving almost nobody — wasted energy.

## Slide 5
KPI 5 — Packet Loss % and KPI 6 — DL Throughput Mbps
Data quality and speed. These confirm what PRB and SINR suggest — if data is actually flowing well.
5
KPI 5 — Packet Loss % (packet_loss_pct)
What percentage of data packets sent by the network are being dropped (lost)?
Simple definition: Imagine sending 1000 letters. If 5 never arrive, packet loss = 0.5%. For video calls and downloads, even 1% loss causes buffering and poor quality.
0.00 – 0.05 %
Excellent
Healthy network, no congestion
0.05 – 0.25 %
Acceptable
Watch — mild congestion building
0.25 – 1.0 %
Degraded
Cell getting congested or interference
> 1.0 %
Severe
SINR_LOW or OVERLOAD — act now
How it's computed in simulator: pkt_loss = max(0, (load - 0.75) x 2.5) — zero below 75% load, rises sharply above
KPI 6 — DL Throughput Mbps (dl_throughput_mbps)
How fast is actual downlink data flowing to users right now (megabits per second)?
Simple definition: The internet speed the tower is delivering. 5G NR peak: 3800 Mbps. 4G LTE peak: 150 Mbps. Affected by both load and signal quality.
< 200 Mbps
Very low
4G cell OR interference — check SINR
200 – 1000
Moderate
5G at low load or 4G at peak
1000 – 2500
Good
5G normal daytime operation
> 2500 Mbps
Excellent
5G peak performance — near full PRB
How it's computed: throughput = (prb_dl_pct / 100) x peak_dl_mbps x jitter Key signal: Low throughput DESPITE high PRB = interference stealing efficiency
LSTM insight: Packet loss rising + throughput falling while PRB stays high = congestion (OVERLOAD). Low throughput with low PRB = interference (SINR_LOW). These patterns are invisible to single-threshold rules.

## Slide 6
KPI 7 — CQI | KPI 8 — BLER % | KPI 9 — Latency ms
Channel health indicators. Added in the latest model update. Richer signal for interference detection.
6
KPI 7 — CQI (cqi)
Channel Quality Indicator
Simple definition: A score from 0 to 15 that tells the tower how good the connection to each user is right now. The tower uses this to choose how fast to send data. Think of it like a Wi-Fi bars indicator — 15 bars = perfect, 0 bars = terrible.
0 – 4
Very poor
Interference or severe fading
5 – 7
Poor
Degraded — check SINR
8 – 11
Moderate
Normal loaded conditions
12 – 15
Excellent
Clean channel, idle or low interference
Computed from SINR: CQI = (sinr_db + 5) / 2.5 — drops fast when signal degrades
KPI 8 — BLER % (bler_pct)
Block Error Rate
Simple definition: What percentage of data blocks (chunks of data) have errors and must be resent? High BLER wastes capacity — the same data is sent multiple times. Like resending a corrupted text message — wastes time and reduces effective speed.
< 2 %
Excellent
Target range — clean delivery
2 – 5 %
Acceptable
Some retransmissions
5 – 10 %
Elevated
Congestion or signal issues
> 10 %
High
SINR_LOW or severe OVERLOAD
Computed: bler = (load - 0.75) x 15 + (10 - cqi) x 0.5 — rises sharply near capacity
KPI 9 — Latency ms (latency_ms)
Cell Round-Trip Latency
Simple definition: How long does it take for a single data packet to travel from the tower to a phone and back? Lower is always better. Like ping time in online gaming — 10ms = fast, 200ms = laggy.
< 15 ms
Excellent
5G NR normal — ultra-low latency
15–30 ms
Normal
Healthy loaded operation
30–60 ms
Elevated
Congestion building up
> 60 ms
High
OVERLOAD — too many users
Computed: latency = 8 + load x 25 + max(0, 5 - sinr) x 2 — rises with load and SINR drop
These 3 KPIs were ADDED in the latest model update (git pull — train.py update, N_FEATURES: 6 -> 9). They give the LSTM a richer picture of interference vs congestion, especially for distinguishing SINR_LOW from OVERLOAD at the boundary.

## Slide 7
5 Extra KPIs — Stored in InfluxDB but NOT Fed to the LSTM
du_simulator.py pushes these to 'cell_kpi' measurement. Used by Grafana dashboards and Orchestrator queries.
7
UL Throughput Mbps ul_throughput_mbps
Uplink speed — how fast users upload data TO the tower. Typically 20-25% of DL throughput (asymmetric network design).
0 – 1000 Mbps
Not fed to LSTM — upload problems are rare and usually mirror DL issues.
Grafana: UE Analytics panel. Helps detect asymmetric congestion.
RSRP dBm rsrp_dbm
Reference Signal Received Power — absolute received signal strength at the UE. Stronger (less negative) = UE is physically closer to the tower.
-120 to -60 dBm
Not fed to LSTM — SINR already captures signal quality more completely.
Grafana: Cell KPI panel. Used for handover decisions and coverage analysis.
PRB UL % prb_ul_pct
Uplink Physical Resource Block usage — how much upload capacity is occupied. Usually much lower than DL PRB in typical consumer traffic patterns.
0 – 95 %
Not fed to LSTM — highly correlated with DL PRB so adds little new information.
Grafana: Cell KPI panel. Useful for IoT/mMTC cells that are uplink-heavy.
HO Success Rate ho_success_rate
Handover Success Rate — what fraction of phone-to-phone-tower switches complete without dropping the call. Target: > 96%. Drops indicate signalling problems or coverage holes.
0 – 100 %
Not fed to LSTM — captures rare events that are hard to model in 60s windows.
Grafana: Network Overview. Alerts if drops below 96% threshold.
Coverage Radius m coverage_radius_m
Estimated RF coverage radius computed from COST-231-Hata path loss model. Larger radius = lower frequency band (n28 700 MHz vs n78 3500 MHz).
200 – 2000 m
Not fed to LSTM — static per cell, does not change at runtime. Config-time only.
Used by Planning API for capacity planning and DU assignment.
Extra KPI
Definition
Where it is used
All 14 cell_kpi fields flow through InfluxDB. The KPI agent reads only the 9 it needs. Grafana dashboards visualise all 14.

## Slide 8
7 DU-Level KPIs — Infrastructure Health of Each Distributed Unit
Written to 'du_kpi' measurement in InfluxDB every tick. Covers compute, memory, fronthaul, and signalling.
8
active_ues
Total UEs
Total number of phones connected across all cells on this DU right now.
DU-MLS-1 (12 cells): 0 – 10,800
Sum of connected_ues per cell. High = DU is busy.
cell_count
Active Cells
How many cells are currently assigned to and active on this DU.
8 – 12 cells
Changes when KPI agent moves cells between DUs.
cpu_pct
CPU Usage %
How much of the DU's processing power is used. L1/L2 baseband processing is CPU-heavy.
0 – 100 %
cpu = 20 + load x 62. High at peak hours or after cell additions.
memory_pct
Memory Usage %
How much RAM the DU is using. Stores UE contexts, buffers, scheduling queues.
0 – 100 %
memory = 30 + load x 45. Spikes if many cells assigned.
fronthaul_latency_us
Fronthaul Latency
Delay in microseconds on the eCPRI/CPRI link between DU and RU (radio unit on the tower).
50 – 200 microseconds
Must stay below 100 us for 5G NR timing requirements.
processing_delay_ms
Processing Delay
Time the DU takes to process one L1/L2 scheduling cycle.
0.1 – 0.9 ms
Increases under high CPU load. > 1 ms causes scheduling jitter.
f1_msg_per_sec
F1 Messages / sec
Rate of F1-AP control messages exchanged between the DU and CU over the F1 interface.
0 – 20,000 / sec
f1_rate = active_ues x 0.5–2.0. Peaks during handovers and reconfigs.
Field
Name
Definition
Range
How computed / note
DU KPIs are NOT fed to the LSTM. They are monitored via Grafana (du_cu_performance dashboard) and used by the Orchestrator's query_network tool to report DU health to the LLM.

## Slide 9
KPI Signatures — What Each Health State Looks Like in the Data
How the LSTM learned to associate KPI patterns with the 5 health states (from train.py class specs)
9
Health State
PRB DL %
SINR dB
UEs
Power W
Pkt Loss %
Tput Mbps
CQI
BLER %
Latency ms
NORMAL (5G)
55%
20 dB
350
520 W
0.05%
1400
11
1.5%
12 ms
OVERLOAD (5G)
94%
11 dB
720
940 W
0.85%
3100
7
8.0%
38 ms
UNDERLOAD (5G)
9%
24 dB
20
330 W
0.01%
190
14
0.3%
9 ms
SINR LOW (5G)
54%
1 dB
290
580 W
1.60%
720
3
12%
45 ms
POWER WASTE (5G)
13%
24 dB
8
880 W
0.01%
145
14
0.2%
9 ms
Red cells = the KPI values that are most diagnostic for that health state. The LSTM learns to recognise these patterns across 6 consecutive timesteps — not just the snapshot values shown here, but the TREND leading up to them.

## Slide 10
Summary — Full KPI Inventory of the KPI Agent
21 total KPIs collected and used across the Malleswaram 4G/5G deployment
10
9 LSTM Input KPIs
Fed to AI model every cycle (model.py FEATURE_NORM)
1. prb_dl_pct — Cell busy-ness %
2. sinr_db — Signal clarity (dB)
3. connected_ues — Active phones
4. power_w — Electricity used (W)
5. packet_loss_pct — Dropped data %
6. dl_throughput_mbps — Downlink speed
7. cqi — Channel quality score
8. bler_pct — Retransmission rate %
9. latency_ms — Round-trip time (ms)
5 Extra Cell KPIs
Stored in InfluxDB / Grafana (not LSTM input)
10. ul_throughput_mbps — Upload speed
11. rsrp_dbm — Signal strength (dBm)
12. prb_ul_pct — Upload capacity used %
13. ho_success_rate — Handover success %
14. coverage_radius_m — RF coverage area (m)
7 DU Infrastructure KPIs
Per Distributed Unit health ('du_kpi' measurement)
15. active_ues — Total connected UEs
16. cell_count — Cells on this DU
17. cpu_pct — CPU usage %
18. memory_pct — RAM usage %
19. fronthaul_latency_us — DU-to-RU delay
20. processing_delay_ms — Scheduling delay
21. f1_msg_per_sec — F1 interface rate
KPI Agent uses 9 of 21 KPIs for AI classification · All 21 flow through InfluxDB · Grafana shows all via 5 dashboards · Orchestrator LLM queries any of them via query_network / query_cell tools