## Slide 1
LSTM KPI Classifier
Explained Simply
How AI watches 30 cells every 10 seconds and keeps the Malleswaram network healthy
NORMAL
OVERLOAD
UNDERLOAD
SINR LOW
POWER WASTE
agents/kpi_agent/model.py | train.py | kpi_agent.py
1

## Slide 2
The Problem — Why Not Just a Threshold Rule?
A single reading misses trends. The LSTM reads 60 seconds of history.
2
RULE-BASED (current fallback)
IF prb_dl_pct > 85% THEN OVERLOAD
Looks at ONE reading at t=now PRB = 86% at t=now → fires OVERLOAD alert immediately But what if PRB was 87% last second and is now DROPPING back to 70%? False alarm — no real problem!
Misses trends · False alarms · Acts too late
LSTM (AI model)
Reads the last 6 readings (60 seconds)
t-50s
60%
t-40s
68%
t-30s
75%
t-20s
82%
t-10s
89%
t=now
94%
Trend: PRB rising consistently for 60s Predicts OVERLOAD BEFORE it peaks Acts while there is still time to move the cell to a lighter DU
Catches trends early · Fewer false alarms · Proactive action
VS

## Slide 3
What the LSTM Sees — 9 KPI Features × 6 Timesteps (60 seconds)
Each cell gets one reading every 10 s → 6 readings = 1 input tensor (shape: 1 × 6 × 9)
3
Feature / Timestep
t-50s
t-40s
t-30s
t-20s
t-10s
t=now
PRB DL % (0 – 100 %)
52%
55%
58%
57%
54%
53%
SINR dB (-5 – +30 dB)
17.2
16.8
17.1
17.5
16.9
17.3
Connected UEs (0 – 800)
312
318
325
320
315
322
Power W (0 – 1200 W)
491
495
502
498
493
496
Packet Loss % (0 – 5 %)
0.03
0.04
0.03
0.05
0.04
0.03
Throughput Mbps (0 – 4000 Mbps)
1230
1260
1285
1270
1240
1255
CQI (0 – 15)
11
11
10
11
11
11
BLER % (0 – 30 %)
1.4
1.5
1.3
1.5
1.4
1.4
Latency ms (0 – 500 ms)
12
13
12
11
13
12
All 54 values (9 features × 6 timesteps) are normalised to [0, 1] before feeding to the LSTM
model.py constants
SEQ_LEN = 6 (6 timesteps) N_FEATURES = 9 (9 KPI fields) N_CLASSES = 5 (output labels) Input shape: (1, 6, 9) batch × time × feat

## Slide 4
Normalisation — Making All Values Comparable
Raw KPI values have very different scales. Normalise everything to 0–1 before the LSTM sees it.
4
normalised = ( value - minimum ) / range
Feature
Raw Value
Min
Range
Normalised
Meaning
PRB DL %
94
0
100
0.94
Near full capacity
SINR dB
2
-5
35
0.20
Poor signal quality
Connected UEs
720
0
800
0.90
Heavily loaded
Power W
880
0
1200
0.73
High but not peak
Pkt Loss %
0.85
0
5
0.17
Some congestion
Throughput Mbps
3050
0
4000
0.76
Good throughput
CQI
7
0
15
0.47
Degraded channel
BLER %
8.0
0
30
0.27
Elevated errors
Latency ms
38
0
500
0.08
Normal latency
Why? — PRB is 0-100, Power is 0-1200, Latency is 0-500. Without normalisation the LSTM would learn 'power matters more' just because its numbers are bigger.

## Slide 5
Inside One LSTM Cell — Gates and Memory
Three gates decide what to remember, what to forget, and what to pass forward at each timestep
5
CELL STATE — Long-Term Memory (carries information across all 6 timesteps without vanishing)
FORGET GATE
What from the past is no longer relevant?
Example: "Last hour's off-peak load data — forget it. Current peak hour is what matters."
INPUT GATE
What new information should I remember?
Example: "PRB just jumped from 60% to 89%. That spike is important — store it."
OUTPUT GATE
What do I pass to the next timestep?
Example: "Rising PRB trend over 5 timesteps — send that signal forward."
HIDDEN STATE — Short-Term Memory (output of this timestep, passed as input to the next)
The CELL STATE solves the 'vanishing gradient' problem — it carries signals across many timesteps without losing them, so the LSTM can learn from events that happened 50 seconds ago.

## Slide 6
Bidirectional — The LSTM Reads Forward AND Backward
Two LSTMs run in parallel. Their outputs are concatenated → richer context.
6
t-50s PRB 60%
t-40s PRB 68%
t-30s PRB 75%
t-20s PRB 82%
t-10s PRB 89%
t=now PRB 94%
Forward LSTM → reads t-50s ... t=now
"PRB is climbing steadily — this looks like sustained overload building up"
Backward LSTM ← reads t=now ... t-50s
"At t=now PRB=94% (confirmed peak). Earlier values confirm the trend was real, not a spike"
Concatenate forward + backward outputs → 128-dimensional vector (64 forward + 64 backward hidden units)
Result: OVERLOAD predicted at 97% confidence The backward pass confirmed the trend was real, not noise

## Slide 7
Full Architecture — From Raw KPIs to a Classification Decision
Two stacked bidirectional LSTM layers followed by a two-layer MLP head
7
INPUT TENSOR
Shape: (1, 6, 9) — 1 cell × 6 timesteps × 9 normalised KPI features
BiLSTM LAYER 1 (hidden=64, bidirectional)
Reads each of the 6 timesteps in both directions → output shape (1, 6, 128) [ 64 fwd + 64 bwd ]
BiLSTM LAYER 2 (hidden=64, bidirectional, dropout 25%)
Deeper temporal abstraction → output shape (1, 6, 128) · dropout prevents overfitting
TAKE LAST TIMESTEP out[:, -1, :]
Extract only the final timestep's combined state → shape (1, 128) · this is the 'summary' of the whole 60s
LINEAR 128 → 64 + ReLU + Dropout 25%
First MLP layer: compress and non-linearise the LSTM output
LINEAR 64 → 5
Second MLP layer: project to 5 output scores (one per class)
SOFTMAX → Probabilities
Convert raw scores to probabilities that sum to 1.0 e.g. [NORMAL 0.04, OVERLOAD 0.93, ...]
model.py KPIClassifier · Total parameters ≈ 145 K · Trains in ~2 minutes on CPU (50 epochs, 5 000 synthetic samples)

## Slide 8
5 Output Classes — What Decision Does the LSTM Make?
Softmax outputs a probability for each class. The highest probability wins. MIN_CONFIDENCE = 70%.
8
0
NORMAL
70% of real cells
PRB 40-70% · Good SINR · Stable UEs
No action needed. Network is healthy.
1
OVERLOAD
15% of real cells
PRB >85% · Packet loss rising · Many UEs
Auto-move cell to lightest available DU
2
UNDERLOAD
8% of real cells
PRB <20% · Very few UEs · Wasted capacity
Flag as sleep candidate (energy saving / DTX)
3
SINR LOW
5% of real cells
SINR <5 dB · High BLER · Low CQI
CRITICAL alert + request PCI re-optimisation
4
POWER WASTE
2% of real cells
High power draw · Very few UEs (<15)
WARNING alert + recommend DTX / sleep mode
Class
Frequency
Typical KPI Signature
SON Action
Frequency is the realistic class distribution used in training (train.py CLASS_COUNTS). Weighted sampler ensures rare classes are learned even at 2%.

## Slide 9
Training — How the Model Was Taught
Synthetic data generated from two separate profiles: 5G NR (64T64R) and 4G LTE (4T4R) · 60 epochs
9
Class Distribution
NORMAL
3,500 (70%)
OVERLOAD
750 (15%)
UNDERLOAD
400 (8%)
SINR LOW
250 (5%)
POWER WASTE
100 (2%)
Two Sub-profiles per Class
5G n78
4G B3/B40
NORMAL power
520 W
120 W
OVERLOAD UEs
720
230
UNDERLOAD PRB
9%
8%
SINR_LOW BLER
12%
10%
PW_WASTE power
880 W
175 W
Generate
5 000 sequences (5G + 4G) 6 steps each
Shuffle
Random permutation to mix classes and technologies
Sample
WeightedRandom- Sampler balances rare classes
Train
60 epochs Adam + Cosine lr annealing
Save
kpi_model.pt Loaded at container start
Temporal drift added between timesteps so the LSTM learns trends, not just point-in-time snapshots | 80/20 train/val split | Gradient clipping at 1.0

## Slide 10
Live Pipeline — From a Cell Reading to an Automated SON Action
Every 10 seconds per cell · 30 cells · first 60 s uses rule-based fallback
10
DU Simulator (or real DU)
Pushes cell_kpi to InfluxDB every 10 s
InfluxDB
Stores time-series KPI telemetry for all 30 cells
KPI Agent polls /query
Reads latest 9 KPI fields for each cell
Sliding Buffer (deque maxlen=6)
Appends reading. Full after 60 s. Older readings drop off.
Normalise + LSTM Infer
9 raw values → normalised → model(x)
Softmax Probabilities
[0.04, 0.93, 0.01, 0.01, 0.01] conf=93%
SON Action
OVERLOAD: Move cell to lightest DU
Confidence gate: if conf < 70% (MIN_CONFIDENCE) — log only, do NOT act
First 60 s: Rule-based fallback (buffer not full yet)
OVERLOAD
Move cell to lightest DU Cooldown: 30 s between moves
UNDERLOAD
TRAFFIC_STEER SON action Recommend handover to enable DTX
SINR LOW
CRITICAL alert Request PCI re-optimisation from Planning API
POWER WASTE
WARNING alert DTX_RECOMMEND: estimated 35% power saving
SON actions are also written to InfluxDB 'son_actions' measurement for audit and Grafana dashboard visibility
NORMAL cells: no action — cycle logs: "Cycle N | cells=30 | normal=24 | overload=4 | underload=1 | sinr_low=1 | pwr_waste=0"